## Slide 1
Agenda
Install and run gridsim.
Create publisher and subscriber ROS nodes.
Move gridsim agent using keyboard over ROS topics.
Move gridsim agent using audio recognition over ROS topics.

## Slide 2
Are you familiar with?
Ubuntu 14.04 Command line/Terminal
  Use VirtualBox if OS X
ROS Indigo
  Install: http://wiki.ros.org/indigo/Installation/Ubuntu
Catkin
ROS Topics: Publishing & Subscribing
Python
  Use 2.7
Git/Github

## Slide 3
Tutorial 1 ROS + gridsim
Clone gridsim repository and install pygame.
  $ git clone https://github.com/u-t-autonomous/gridsim.git
  $ sudo apt-get install python-pygame swig bison cython autoconf python-pyaudio
Create a 5x5 gridworld with one agent and no obstacles (see config.txt).
Write a script to control the agent using the keyboard (use keyboard_tutorial1.py).
Create catkin workspace.
  $ mkdir catkin_ws
  $ cd catkin_ws
  $ catkin_init_workspace
Create a new ROS package.
  $ cd src
  $ catkin_create_pkg wiald std_msgs rospy

## Slide 4
Tutorial 1 ROS + gridsim
In catkin_ws/src/wiald/src:
Create a subscriber node (edit subscriber_tutorial1.py).
  The node subscribes to /cmd.
  The callback in the subscriber node moves the agent accordingly every time there's a new message in /cmd.
Create a publisher node (edit publisher_tutorial1.py).
  The node gets the user's input from the keyboard.
  The node publishes to /cmd.
Make both nodes executable
  In catkin_ws run $ catkin_make
  In wiald/src run $ chmod +x xx.py
Run the nodes and move the agent around using the publisher/subscriber nodes using the keyboard.
  $ rosrun wiald subscriber_tutorial1.py
  $ rosrun wiald publisher_tutorial1.py
  $ roscore

## Slide 5
Tutorial 2 Audio Recognition + ROS + gridsim
Install audio recognition package.
  $ sudo apt-get install swig bison cython autoconf, python-pyaudio
  $ git clone https://github.com/u-t-autonomous/HCI-testbed.git
  Install sphinxbase, pocketsphinx from: https://sourceforge.net/projects/cmusphinx/files/
  Run ./autogen.sh, make, sudo make install to install the above
  $ export LD_LIBRARY_PATH=/usr/local/lib:/opt/ros/indigo/lib
Create a publisher node (edit publisher_tutorial2.py).
  The node gets the user's input from the microphone.
  The node publishes the user's input to /cmd.
Make the node executable
  $ chmod +x xx.py
Use the subscriber node from the previous tutorial (subscriber_tutorial1.py).
Run the nodes and move the agent around using the publisher/subscriber node with your voice.
  $ rosrun wiald subscriber_tutorial1.py
  $ roslaunch pocketsphinx move.launch
  $ roscore